## Slide 1: IPv6 for Internet service providers state/lessons/still to come
Aaron Hughes, CEO 6connect
aaron@6connect.com
RIPE70

## Slide 2: Perception of ipv6 implementations
Network People
  “We dual stacked the network years ago and we’re done”
Sales People
  “Yes, we have that”
DevOps
  “We don’t really need to do anything” – “Do I need to be doing anything?”
Systems Support staff
  “All we have to do is turn it on and HUP the process”
Cloud Providers
  “We can get you an IPv6 address”..

## Slide 3: Exploring realities
After conducting interviews with various type of providers in the Service Provider space, I’ve found that reality does not match perceptions.
While we in the operator and policy forums are focused heavily on dual stacking backbones, eyeballs and eyeball facing content, the reality of percentage of implementation is different than perception.
The globally acceptable metric in these forums seems to be percentage of IPv6 traffic on the global internet measured by, typically, Google.
While measuring actual implementation with ISPs may be challenging, this is an attempt to give the state of some ISPs, where they are today, difficulties, and general experiences.
If this is useful, it may be useful to have regular polls in an anonymous format for Service Providers (and perhaps Enterprises) to provide to this audience.

## Slide 4: A small Canadian ISP
Our IPv6 plan was phased over time
We started with our BGP core adding transit and peers over time
As part of server refreshes, we enabled IPv6 functionality over time.
A byproduct of the migration has been the cleanup of a number of outlier systems and network components.
We didn't have a large lab to test everything so we would change a small part each time and watch for issues.
To date a couple minor bugs but no customer facing concerns.

## Slide 5: A small Canadian isp cont.
Routers
Switches
BACKEND Monitoring
DNS (recursive)
DNS (authoritative)
MAIL
Control Panel Web Servers
Radius
Backup Servers
VPN
Corporate Firewall

## Slide 6: A small Canadian isp cont.
Things we learned along the way:
1) The Big Unknown. Older Servers and Routers need to be updated or refreshed.
Stateful Firewall for IPv6 not supported in Redhat 5 (No Connection Tracking).
Feature parity in older JunOS versions weren't there.
FreeRadius 1.x doesn't support sending IPv6 packets.
2) It's the small things
fail2ban a firewall script for blocking doesn't have IPv6 support (experimental only)
Custom scripts written years ago were making IPv4 assumptions.
We use greylisting and utilize whitelisting, very limited IPv6 support.

## Slide 7: A small Canadian isp cont.
3) Reverse DNS is a bind 
We migrated to PowerDNS to simplify IPv6 reverse delegation.
4) Have a plan for your netblock
A /32 is a lot of space for a small ISP, unless you divide it badly. We split ours into a /36 per POP. Each business customer is sparse allocated a /48.
5) The final step is the enabling of IPv6 for our DSL and Fibre customers, as this has the most devices outside of our control.

## Slide 8: A medium sized provider in California
Dual stacking the backbone was easy.
  We started with peers early on (HE was a huge help since they provided full tables)
  Transit was harder to get and took time to get them to execute (6 months for all transit providers to get completed)
Subnet size challenges for PTP (/127 v /126 v /64)
  Initially used /64s, switched to /126s after hearing about TTL bouncing attacks. Chose 126 over 127 to keep operation staff comfortable with ::1 ::2 (discarded the rest of the 64) (Didn’t like the idea about :: (or ::0) as a valid address.
  Over time converted back to 64s on all interfaces and 48s to customers via static.

## Slide 9: A medium sized provider in California
After dual stack was completed, added a few SLAAC subnets in lab environments and quickly added public facing services (NS, MAIL, WEB)
Writing IPAM was a painful process e.g. get next approach different from IPv4
Internal tools took some time to update and training sales and SEs to add fields in Salesforce for IPv6 allocation ($0 line item) was challenging to explain.
Selling the story internally to all staff was like talking about the Y2K issue. People simply didn’t believe we were really in need of making serious changes.
Customer “demand” trickled in slowly over time and implementation staff received real world experience with turn-ups including customer BGP inet6, etc.
Took an additional year to get supporting internal services dual stacked.

## Slide 10: A medium sized provider in California
Supporting systems were difficult
  Training ops on PTRs for ip6.arpa. / Delegation not easy.
  Were using IRRPT for customer filters, no support for v6
  Many hard coded references in code, logging analysis, abuse reporting, etc
  No monitoring tools available to properly externally monitor dual stack.
    Added additional probes per host with hard coded stack
    Still a work in progress with external monitoring orgs.
    Debating service.ipv4.domain.com & service.ipv6.domain.com
      Name Based virtual hosts with application testing extremely difficult.
    Internal monitoring was less of an issue, but still no decent discovery of v6 subnets and hosts within. Displaying stacks on visuals is still a challenge.
    Debugging which stack is being used not being relayed clearly to support.

## Slide 11: A medium sized provider in California
IPv6 not engrained in decision making
  Getting entire company to require proper support from vendors (not make the problem worse) is very hard to instill
    Not willing to put the relationship on the line for IPv6 support.
  Constant reminders to provisioning staff that dual stack must be the default assignment is getting better, but still not part of normal behavior
  Convincing sales to charge more money for IPv4 statics and give IPv6 without cost is difficult. They don’t want to confront the “why” we are charging more with the customer(s).
  Eating your own dog food is not enough to get people to understand the underlying differences.

## Slide 12: A medium sized provider in California
Downstream Training:
Educating prospects and existing customers is an uphill battle
  Sales staff does not want to risk potential revenue by injecting IPv6 into RFP requirements.
  The level of comfort with discussing downstream customers IPv6 plan is low. There is a fear that the dialogue can interfere with margin or cause them to feel unhappy
  Additional fears / discomfort with potentially disclosing how much IPv4 space is in our own inventory (The customer may go somewhere with more inventory).

## Slide 13: A medium sized provider in California
Feature Parity
  Seemingly simply features in IPv4 are not supported with IPv6 on a great deal of hardware and software (or supporting software)
    Cisco HSRP (standby version 2)
    Stateful firewalls
    Load balancers
    IPS/IDS/Security analysis tools (and alerting)
    FlowAnalysis
    Log Parsing tools
    Filtering tools
    DNS management tools
    DHCPd (and helper addresses)
    Odd behaviors with v4 NAT + v6 Native (inconsistent security policies)

## Slide 14: A medium sized provider in California
Internal supporting staff
  Very limited number of operations and IT staff able to understand how to debug IPv6 and dual stack issues.
  Even fewer able to train others
  DevOps staff consider requests ‘new features’ vs. ‘bug’ and have long timelines.

## Slide 15: A medium sized provider in California
Security
  Entirely different to secure
  Duplication of policies does not always work
  NAT is no longer the demarc and requires unique policy
  Some applications only bind to IPv4 and avoid the security application entirely
    Symantec Encryption Desktop / PGP issues
  Duplicating security policy challenges

## Slide 16: A cloud service provider
Orchestration platforms missing IPv6 support entirely.
  vCenter, vRemote, etc, zero support for IPv6
Defining vCell IP schema difficult, matching to existing 1918 plan
Could not add management network without public facing first
  If a server has an IPv6 address, it will attempt to use the AAAA’s of those returned.
DNS policies utilizing split horizon need to change
Mapping solutions for things such as OpenStack UUID (mgmt ssh broken)
Most provisioning tools are home-grown dev-ops v4 only
Missing ILMI support over v6 on a ton of gear

## Slide 17: Eyeball access
All connected Ethernet type services were easy to dual stack (bridged)
DSL and cable modems have mixed support and behavior
  Feature parity missing with 100% of vendors based on received feedback
    Missing firewall, mapping, MAC filtering, security features
Allocation sizes to customers vary from a single /64 to a /48.
Surprising majority only hand out a single /64
Support for static v6 assignments missing from most eyeballs.
  Long DHCP leases were the norm
  Several waiting on CMTS support for IGP features.

## Slide 18: Backbone topology
Overwhelming majority:
  OSPFv3 on loopbacks and connected links
  iBGP injecting other connected interfaces and static routes
  eBGP aggregation of aggregates
  Most started with dual stacking the backbone, adding peers or transit and working their way in from edge to core
  Most added test systems and then some public facing services
  Most added operations staff for purposes of comfort
  Most then considered this a stopping point for a long time while working on internal education and approaching all other services and equipment over long periods of time.

## Slide 19: conclusions
ISPs have had no trouble dual stacking their backbones
Major public facing services were mostly easy to deploy
There is still a great deal of work to do with hardware and software vendors
Many vendors claim support which simply does not work
Completely missing in all evaluated cloud orchestration products
Getting to the next steps (default v6 for all customers, services, educated staff same as v4) is going to take a lot of time.
Continuous work with hardware and software vendors
“IPv6 enabled / compatible” frequently means broken implementations or some portion of IPv6 support
Everyone I spoken to was comfortable talking about their experiences and naming specific vendors with issues as long as they were anonymous.

## Slide 20: Questions / comments ?