## Slide 1: The Role of Analytics in Routing, Network Performance and SDN Cengiz Alaettinoglu

## Slide 2: It all started with a jitter study (2000)
Studied jitter on 3 US and 1 European backbones for several weeks
For 99.99% packets, measured jitter < 1ms

## Slide 3: However, 0.01% of Jitter was severe
10+ seconds packet drops
7 seconds jitter
Severe packet reordering

## Slide 4: Theory: Packets being spewed out from an unwinding routing loop…
Did we really have long routing loops in the network?
Did ISIS really take 10+ seconds to converge?
So, we analyzed routing along with jitter
Test host is
passive peer,
sends no routes
IP Backbone
R
traceroute
every 5s
ISIS
hellos +
tcpdump
traffic
Test Host
packet
trace
file
sk
gig-ether
Test Host
R

## Slide 5: ISIS in a Nutshell
Each router sends Link State Packets (LSP) that describes its local topology
  List of links to neighbors (adjacencies), prefixes along with metrics
  This is refreshes periodically, otherwise LSP content is purged
This is flooded across the network
  Each router send new LSPs it receives to its neighbors
  Neighbors sends to their neighbors, …
Each router accumulates LSPs into a database (LSDB) and constructs the current view of the topology
Shortest paths are computed using Dijkstra's SPF algorithm

## Slide 6: Excessive ISIS churn caused excessive LSP Propagation Delay
All link state packets (LSPs) including refreshes
LSPs that report a change
LSP propagation delay
Seconds between seeing the same LSP in the east and the west coasts of the US

## Slide 7: Explanation
Link state databases were not in sync:
  Very large LSP databases
  High churn rate caused many LSPs to flood
  LSP rate-control slowed down flooding
  Any topology change could result in a loop under these conditions
We realized being able to look at routing was key for powerful network performance analysis
Today, we see very high churn in very large TE databases using auto-bandwidth with large number of tunnels

## Slide 8: Route Analytics Today
Collection
Analysis
Presentation
BGP
IGPs
Flows
Multicast
. . .
Path Reports
RCA
Exit Routers
Traffic Reports
. . .
. . .
Tunnels
Reporting
Alerting
Planning
Trouble-
shooting
Troubleshooting and visualization
Service/application monitoring and alerting
Network health assessment
Topology-aware traffic analysis
Proactive change modeling
Analytics-driven Software Defined Networking applications

## Slide 9: Use Case: Diagnosing Black Holing
A peering router to a major service provider crashed
  Hot swappable card was not quite so…
Traffic to the SP was black-holed network-wide
  Traffic exiting all 6 locations was black-holed
About 3 minutes of routing outage
  3 minutes was too short to diagnose the issue at human speed
  Had a 45 minute impact on the services and ad revenues
    Users who could not use the service did something else

## Slide 10: Expected Exit-Points Before Incident
6 Exit-Points (circled)
Blue routers take the blue exit router…

## Slide 11: Recursive Route Resolution
BGP determines exits
  NextHop attribute
Usually IGP distance determines the closest
More accurately, we recursively find a path to NextHop
  IGP, static, BGP, or a series…
BGP
IGP

## Slide 12: The Incident
ISIS activity during incident

## Slide 13: Exit-Points During Incident
6 more exit-points popped up
  All core routers
  No EBGP

## Slide 14: A Path Before and After the Incident
Before
After
Route Recursion
BGP Next hop resolution: before 128.9.129.1/32 in ISIS vs. after 128.9.128.0/19 in BGP

## Slide 15: Cause of Black Holing
Every SP announces its address space externally in BGP
  128.9.128.0/19 BGP route is for this purpose
  But it also resolves the NextHop address 128.9.129.1/32
When the peering router crashed
  IGP routes from that router were withdrawn in milliseconds
  BGP routes from that router were not withdrawn
    3 KEEPALIVEs of 60 seconds each – router rebooted before this
  These BGP routes were now resolved by 128.9.128.0/19 in BGP
  Injected by 6 core routers
  Distance to a core router from any router is very low
  Every router uses the dead router’s BGP routes
We are good at designing networks when everything is up and running, but failure cases are often beyond our imagination

## Slide 16: Remedy
Insert a really expensive static route for the /19 to ISIS
  It should cost more than longest possible path in IGP
  ISIS routes preferred over BGP routes and will hide the /19 BGP route in recursion
  Now, when a peering router crashes, the traffic will choose a true exit
  See: http://www.nanog.org/meetings/nanog34/presentations/gill.pdf
Do not: Make IBGP session converge faster (like running BFD)
  One may argue the root cause is that BGP was too slow to withdraw
  You will lose the IBGP session each time the IGP path of the session changes

## Slide 17: Challenges in Operating SDN
What governs whether or not these programmatic changes should be made? What will be their impact?
SDN makes networks programmable for
Network overlays
Bandwidth reservation
Demand placement
Service deployment
Etc.
-- but --
Physical & Virtual Routers, Switches & Network functions
Applications
Bandwidth Calendaring
Demand Placement
Service Deployment
ETC.
SDN CONTROLLERS
Southbound APIs: OpenFlow, i2RS, PCE, NETCONF, ForCES, SNMP, CLI, etc.
Northbound APIs

## Slide 18: Need for Analytics-Driven Applications
When major apps/services are introduced, planning groups validate capacity
  Quality of Experience expectations
  Capacity planning
  Changes to the topology, CoS treatment, …
If the apps/services are being rolled out without operator intervention, how do you plan for them?
  SDN analytics addresses this concern

## Slide 19: How Rich Analytics Help a Bandwidth Scheduling Application
Bandwidth scheduling: can I move X bps from A to B at time t ?
Attractiveness: SPs have abundance of spare bandwidth
  Most SP networks have less than 50% utilization
    Verizon: 46% average peak utilization
    Level 3: 46-56% peak utilization range
Can an SP profit from this spare capacity?
But there are good reasons for this spare bandwidth

## Slide 20: A Naïve Implementation
Let’s collect link utilizations
  This is near real time; and SPs already have it
We need utilizations at time t
  Use historical link utilizations
  Baseline: average same 5-minute or hour of the day for several weeks
  Add projections for growth and safety
Compute path from A to B and add X bps to the links
  Go or no-go decision based on new link utilizations
If go, schedule the SDN controller to set up this path from A to B at time t, and tear it down afterwards

## Slide 21: Reasons for Spare Bandwidth
Increased utilization  increased delay and jitter
  Delay vs. link utilization curve has a sharp knee
Network must accommodate failures
  Network must have capacity to reroute the traffic around failures
  Large networks have one link down at any given time, they must tolerate two link failures
Traffic is growing but adding capacity takes time

## Slide 22: Addressing These Challenges
Increased delay
  Cap the go/no-go decision at ~65-70%
  For anything above that we must be moving bulk traffic
    Not suitable for uncompressed HD broadcast of an event
    Not even suitable for best-effort traffic
    Must deploy differentiated services
Protect against failures via analytics driven simulation
  Fail every (or two) link/router and see the impact on link utilizations
    Not sufficient to fail just the links/routers along the path

## Slide 23: Failure Impact: Where will the traffic go?
We need to know where the traffic is entering the network, how much traffic there is, and where it is exiting the network
  Link utilizations don’t tell where the traffic is entering or exiting the network
We need to understand the network’s routing to compute the new paths

## Slide 24: Need for a Traffic Demand Matrix
Traffic Matrix:
  For each router pair (r1,r2), how much traffic entering at r1 is exiting at r2?
Flow data coupled with routing gives us traffic matrix

## Slide 25: Simulation and Impact of a Failure
For each flow on the failed link
  Go to the ingress router and find the new path for the flow
  Subtract flow’s bandwidth from the old links
  Add flow’s bandwidth to the new links
  Check to see if congestion crept in
We need an accurate routing model of the network
  Route analytics provides this for IGP, BGP, RSVP-TE, VPNs…

## Slide 26: Concluding Remarks
Routing impacts network performance
  Availability and reachability
  Sub-optimal paths with longer delays, jitter
Route analytics proves to be very effective in
  Troubleshooting, monitoring, alerting
  Reporting and network health assessment
  Routing-aware traffic analysis
    BGP peering analysis
    Traffic matrices
Rich analytics are key for successful SDN deployment and applications, including bandwidth scheduling