## Slide 1: Bgpdump2: A Tool for Full BGP Route Comparison
Yasuhiro Ohara
yasuhiro.ohara@ntt.com
NTT Communications

## Slide 2: 20150319 p19 NTT

## Slide 3: Motivation (1)
As a researcher in an ISP ...
Don't we need a way to evaluate a shape of (our) BGP full route routing table ?
Why ?
  Mistakes: missing routes, route leaks, ...
  Better future configuration: roundabout routes
Many things boils down to it
  the routes are good, then we're good.

## Slide 4: Motivation (2)
How can we evaluate a shape of BGP full routes ?
  We don't know it yet.
  detailed (statistical) analysis ?
  compared to others ?
So let's create a tool to help doing those.

## Slide 5: bgpdump2 summary
Full scratch in C (4000- lines)
Open-source software
  <https://github.com/yasuhiro-ohara-ntt/bgpdump2>
Capability:
  supported: bz2, gzip, and raw, MRT TABLE_DUMP_V2 format, ipv4 / ipv6 routes
  show statistics per peers (e.g., #routes, #nexthops, #unique-AS-paths)
  routing table construction, longest-match table lookup

## Slide 6: route collectors and monitors
AS
AS
AS
AS
route collector
route monitor
route monitor
route monitor
eBGP
Peer Table
peer 1
peer 2
peer 3
Routes
1.0.0.0/24
peer 1's attrs
peer 3's attrs
Save
The RIB dump file
out
filter
in
filter

## Slide 7: simple display
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 | head -10
0.0.0.0/0 203.189.128.233 origin_as: 9902 as-path[2]: 23673 9902
1.0.0.0/24 213.144.128.203 origin_as: 15169 as-path[2]: 13030 15169
1.0.0.0/24 198.129.33.85 origin_as: 15169 as-path[2]: 293 15169
1.0.0.0/24 5.101.110.2 origin_as: 15169 as-path[3]: 202018 1299 15169
1.0.0.0/24 162.243.188.2 origin_as: 15169 as-path[2]: 393406 15169
1.0.0.0/24 95.85.0.2 origin_as: 15169 as-path[2]: 200130 15169
1.0.0.0/24 192.241.164.4 origin_as: 15169 as-path[2]: 62567 15169
1.0.0.0/24 129.250.0.11 origin_as: 15169 as-path[2]: 2914 15169
1.0.0.0/24 66.185.128.1 origin_as: 15169 as-path[2]: 1668 15169
1.0.0.0/24 173.205.57.234 origin_as: 15169 as-path[3]: 53364 3257 15169

## Slide 8: Speed
74M routeviews/oregon-ix2/rib.20150319.0000.bz2
% /usr/bin/time -p bash -c 'bzcat routeviews/oregon-ix2/rib.20150319.0000.bz2 > /dev/null 2>&1 '
real 28.98 user 28.80 sys 0.10
% /usr/bin/time -p bash -c 'bzcat routeviews/oregon-ix2/rib.20150319.0000.bz2 | ./zebra-dump-parser/zebra-dump-parser.pl > /dev/null 2>&1 '
real 428.29 user 467.67 sys 1.07
% /usr/bin/time -p bash -c './libbgpdump-1.4.99.11/bgpdump routeviews/oregon-ix2/rib.20150319.0000.bz2 > /dev/null 2>&1 '
real 148.71 user 148.38 sys 0.24
% /usr/bin/time -p bash -c './bgpdump2/src/bgpdump2 routeviews/oregon-ix2/rib.20150319.0000.bz2 > /dev/null 2>&1 '
real 89.09 user 88.74 sys 0.19

## Slide 9: display peer index table
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 -P | head -12
Collector BGP ID: 128.223.51.102
View Name Length: 0
View Name:
Peer Count: 58
# peer_table[0] changed: 0.0.0.0 asn:0 [129.250.0.11|::]
# peer_table[1] changed: 10.10.10.252 asn:53364 [173.205.57.234|::]
# peer_table[2] changed: 0.0.0.0 asn:0 [192.241.164.4|::]
# peer_table[3] changed: 4.69.184.193 asn:3356 [4.69.184.193|::]
# peer_table[4] changed: 5.101.110.2 asn:202018 [5.101.110.2|::]
# peer_table[5] changed: 12.0.1.63 asn:7018 [12.0.1.63|::]
# peer_table[6] changed: 64.57.28.241 asn:11537 [64.57.28.241|::]
# peer_table[7] changed: 66.185.128.1 asn:1668 [66.185.128.1|::]

## Slide 10: display per peer routing table
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 -p 19 | head -8
1.0.0.0/24 129.250.0.11 origin_as: 15169 as-path[2]: 2914 15169
1.0.4.0/24 129.250.0.11 origin_as: 56203 as-path[4]: 2914 3257 4826 56203
1.0.5.0/24 129.250.0.11 origin_as: 56203 as-path[4]: 2914 3257 4826 56203
1.0.6.0/24 129.250.0.11 origin_as: 56203 as-path[4]: 2914 3257 4826 56203
1.0.7.0/24 129.250.0.11 origin_as: 56203 as-path[6]: 2914 3257 4826 56203 56203 56203
1.0.38.0/24 129.250.0.11 origin_as: 24155 as-path[2]: 2914 24155
1.0.43.0/24 129.250.0.11 origin_as: 24155 as-path[4]: 2914 1299 10026 24155
1.0.44.0/24 129.250.0.11 origin_as: 24155 as-path[4]: 2914 1299 10026 24155

## Slide 11: per peer statistics
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 -k | less
:
peer[19]:
Number of routes: 524728
Number of routes per plen:
/0 : 0 /1 : 0 /2 : 0 /3 : 0 /4 : 0
/5 : 0 /6 : 0 /7 : 0 /8 : 16 /9 : 12
/10: 33 /11: 92 /12: 263 /13: 501 /14: 991
/15: 1701 /16: 12887 /17: 7047 /18: 11927 /19: 24655
/20: 35315 /21: 37702 /22: 57644 /23: 49291 /24: 284473
/25: 52 /26: 51 /27: 20 /28: 20 /29: 16
/30: 6 /31: 0 /32: 13
Number of nexthops: 1
Number of origin_as: 49440
Number of unique as paths: 75351
Number of as path len: 39
:

## Slide 12: Distribution in Prefix Length

## Slide 13: routing table lookup (longest-match)
Routing Table (PATRICIA) can be created.
one address lookup.
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 -p 19 -l 8.8.8.8
looking up an address: 8.8.8.8
8.8.8.0/24 129.250.0.11 origin_as: 15169 as-path[2]: 2914 15169
a list of address lookup contained in a file.
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 -p 19 -L ../test-lookup.txt
50.0.0.0/16 129.250.0.11 origin_as: 7065 as-path[3]: 2914 8121 7065
100.0.0.0/16 129.250.0.11 origin_as: 701 as-path[2]: 2914 701
150.0.0.0: no route found.
200.0.0.0: no route found.

## Slide 14: Diffs a peer against others
script/compare-peer-with-others.sh
marks
udiff:
<: the prefix is in left and unreachable in right (maybe partially).
+: the prefix is only in right (but it is reachable in left).
): the prefix is in right, and is covered by a shorter prefix in left
that is unreachable in right. (i.e., the shorter is '<')
>: the prefix is in right and unreachable in left (maybe partially).
-: the prefix is only in left (but it is reachable in right).
(: the prefix is in left, and is covered by a shorter prefix in right
that is unreachable in left. (i.e., the shorter is '>')

## Slide 15: Comparison among peers
diff routes between 2914 and 3356:
>70.61.0.0/20 4.69.184.193 origin_as: 10796 as-path[3]: 3356 7843 10796
>70.61.1.0/24 4.69.184.193 origin_as: 10796 as-path[3]: 3356 7843 10796
>70.61.2.0/24 4.69.184.193 origin_as: 30628 as-path[4]: 3356 7843 10796 30628
(70.61.4.0/24 129.250.0.11 origin_as: 10796 as-path[4]: 2914 2828 7843 10796
(70.61.5.0/24 129.250.0.11 origin_as: 10796 as-path[4]: 2914 2828 7843 10796
(70.61.6.0/24 129.250.0.11 origin_as: 33363 as-path[5]: 2914 2828 7843 33363 33363
+71.29.112.0/21 4.69.184.193 origin_as: 7029 as-path[3]: 3356 2828 7029
>71.44.17.0/24 4.69.184.193 origin_as: 33363 as-path[2]: 3356 33363
>71.44.53.0/24 4.69.184.193 origin_as: 33363 as-path[2]: 3356 33363
>71.44.62.0/24 4.69.184.193 origin_as: 33363 as-path[2]: 3356 33363
-71.252.67.0/24 129.250.0.11 origin_as: 64512 as-path[3]: 2914 701 64512
+72.0.224.0/23 4.69.184.193 origin_as: 19940 as-path[2]: 3356 19940
+72.0.227.0/24 4.69.184.193 origin_as: 19940 as-path[2]: 3356 19940

## Slide 16: missing prefix ranking in AS 2914 in Oregon IX
cat data/oregon-ix2-rib.20150319.0000.bz2-p19/route-diff-rib.20150319.0000.bz2-p19-*-diff.txt | grep '^>' | awk '{print $1;}' | sort -n | uniq -c | sort -n –r
38 >94.176.2.0/24 94.176.2.0 ASTIMP-ASAstimpConsultingSRL,RO
38 >94.176.131.0/24 94.176.131.0 VOXILITY-ASVoxilityS.R.L.,RO
38 >94.156.77.0/24 94.156.77.0 NETERRA-ASNeterraLtd.,BG
38 >94.156.185.0/24 94.156.185.0 NETERRA-ASNeterraLtd.,BG
38 >94.156.184.0/24 94.156.184.0 NETERRA-ASNeterraLtd.,BG
38 >93.123.18.0/24 93.123.18.0 NETERRA-ASNeterraLtd.,BG
38 >93.120.36.0/22 93.120.36.0 VOXILITY-ASVoxilityS.R.L.,RO
38 >93.120.35.0/24 93.120.35.0 ASTIMP-ASAstimpConsultingSRL,RO
38 >93.115.92.0/22 93.115.92.0 VOXILITY-ASVoxilityS.R.L.,RO
38 >93.115.88.0/22 93.115.88.0 VOXILITY-ASVoxilityS.R.L.,RO

## Slide 17: ranking in appearance count of whois descr
180
88 TFN-TWTaiwanFixedNetwork,TelcoandNetworkServiceProvider.,TW
60 VOXILITY-ASVoxilityS.R.L.,RO
60 FPT-AS-APTheCorporationforFinancing&PromotingTechnology,VN
42 SCRR-10796-TimeWarnerCableInternetLLC,US
37 TAIWANMOBILE-ASTaiwanMobileCo.,Ltd.,TW
33 XTGLOBALXTGLOBALNETWORKSLTD.,RO
32 DATAFRAMELO-DataframeLogistics,Inc.,US
28 ONE-NET-HKINTERNET-SOLUTION-HK,CN
24 VNPT-AS-VNVNPTCorp,VN
2914:4429 community tag: do not advertise in Asia.
http://www.us.ntt.net/support/policy/routing.cfm

## Slide 18: full route number
peer 13 was empty.
The R script is also provided.
% sh full-route-number.sh -p 0 -p 1 -p 2 -p 3 -p 5 -p 7 -p 11 –p 13 ../../../routeviews/oregon2-summary/rib.20140{1,2,3}*.bz2

## Slide 19
Increase in the number of route.
Disbribution per prefix length.
2014-08-12 00:00 – 2014-08-13 00:00

## Slide 20: A Use Case (1)
Access source analysis of an open NTP server
  tcpdump: 50M pcap packets
  Solving 50M source IP addresses to Origin ASes
  Whois/DNS query to Team Cymru didn't work.
  bgpdump2 helped it:
  The user's voice: It was good because
    the portability (local resolution from the file),
    the speed was super quick,
    will help in retrospect activities.

## Slide 21: A Use Case (2)
    50 files, each including approx. 1M addresses
      time bgpdump2 $HOME/work/bgp/rib/rib.20150508.0600 -p 0 -L <filename>
    using raw RIB file, cached on memory
    Took 00:03:59.1 (in total) to solve 49,921,136 IP addresses
      3.912u 0.848s 0:05.76 82.4% 0+0k 128+28io 8pf+0w
      3.908u 0.651s 0:04.59 99.1% 0+0k 38+6io 0pf+0w
      4.063u 0.689s 0:04.78 99.1% 0+0k 112+13io 0pf+0w
      3.969u 0.646s 0:04.64 99.1% 0+0k 4+6io 0pf+0w
      4.002u 0.650s 0:04.70 98.9% 0+0k 8+4io 0pf+0w
      4.038u 0.646s 0:04.72 98.9% 0+0k 0+4io 0pf+0w
      4.136u 0.661s 0:04.81 99.5% 0+0k 2+17io 0pf+0w
      :

## Slide 22: Heatmap
Just represents the density of IP reachability
  A.B/16 depicts one point
  In Hilbert Curve
  lookup A.B.C.0 (head address of the /24) in the A.B/16 and counted the number of success (found)
  A (the first octet) is labeled in white

## Slide 23: 20150319 p19 NTT

## Slide 24: 20150319 p3 Level3

## Slide 25: 20150319 p1 ZEROFAIL

## Slide 26: 20150319 p4 Digital Ocean

## Slide 27: 20150319 p5 AT&T

## Slide 28: 20150319 p7 AOL

## Slide 29: 20150319 p8 Level3 (GBLX)

## Slide 30: 20150319 p9 Fibrenoire Internet

## Slide 31: 20150319 p11 TeriaSonera

## Slide 32: 20150319 p12 OBIT

## Slide 33: 20150319 p42 IIJ

## Slide 34: Timemachine: 2015 NTT

## Slide 35: Timemachine: 2014 NTT

## Slide 36: Timemachine: 2013 NTT

## Slide 37: Timemachine: 2012 NTT

## Slide 38: Timemachine: 2011 NTT

## Slide 39: Timemachine: 2010 NTT

## Slide 40: Wrap up
An open-source tool is newly developed to analyze BGP dump: bgpdump2.
  currently support only RIB dump (not BGP updates)
New features
  per peer statistics, per peer display of routes
  diffs
  PATRICIA-based routing lookup (longest-match)
The tool should help:
  BGP route debugging incl. route leaks
  ISP comparison
  analysis, and/or research

## Slide 41: Thanks. Questions ?

## Slide 42: Existing tools
libbgpdump
  written in C. <https://bitbucket.org/ripencc/bgpdump/wiki/Home>
zebra-dump-parser
  written in Perl. <https://github.com/rfc1036/zebra-dump-parser>
java-mrt library
  written in Java. <https://github.com/paaguti/java-mrt>
UCLA bgpparser
  written in C++. <http://irl.cs.ucla.edu/software/bgpparser.html>
mrtparse
  written in Python. <https://github.com/YoshiyukiYamauchi/mrtparse>
openbgpd bgpctl
  written in C. <http://cvsweb.openbsd.org/cgi-bin/cvsweb/src/usr.sbin/bgpctl/>
pybgpdump
  writen in Python. <https://jon.oberheide.org/pybgpdump/>

## Slide 43: libbgpdump compatible mode
not finished: e.g., support for community, localpref, etc., are not yet completed.
% ./src/bgpdump2 ../routeviews/oregon-ix2/rib.20150319.0000.bz2 -m | head -3
TABLE_DUMP2|1426723200|B|203.189.128.233|23673|0.0.0.0/0|23673 9902|INCOMPLETE|203.189.128.233|0|0|0|NAG||
TABLE_DUMP2|1426723200|B|213.144.128.203|13030|1.0.0.0/24|13030 15169|INCOMPLETE|213.144.128.203|0|1|0|NAG||
TABLE_DUMP2|1426723200|B|198.129.33.85|293|1.0.0.0/24|293 15169|INCOMPLETE|198.129.33.85|0|0|0|NAG||